## Slide 1: PORT
In NXP S32K146, there are 5ports.
PORT A, B, C, D, E.
PORT A: 0~31 PORT B: 32~63 PORT C: 64~95 PORT D: 96~127 PORT E 128~159
There are 164 pins in NXP S32K146.
PTD0 -> blue led. -> PORT D 96
PTD15 -> red led -> PORT D 96+15 = 111 (pin number)
PTD16 -> green led -> PORT D 96 + 16 = 112
Each ports contain such of pins

## Slide 2: PORT
PORT = Group of pins
Pull-up = high = logic 1 (on)
Pull-down = low = logic 0 (off)
Pull-desabled = neither logic 1 nor 0 ->floating condition.
If we need to use floating condition pin, we need to change condition by using Pull-up or Pull-down.

## Slide 3: PORT
Addressing: Mapping the right number to the right port.
Usage: choose the port is input or output
ex) if led is blinking -> usage.
I/O operation.
Input: read data Output: send data to actuator

## Slide 4: DIO
DIO (Digital input, output) - microcontroller that handling Digital signal.
1. Digital input: Detect high or low voltage levels high-1 low-0, used to read a switch state.
2. Digital output: drive digital external devices. Output high(VCC), low (ground)
3. Applications: DIO functionalities.
4. Programing Interface: It reads information from pins and interact with external devices.
5. Configuration: input: reading, output: generating

## Slide 5: Tresos
AUTOSAR tool -> choice value(select parameter), then this tool make code automatically.
Tool – configuration bsw(basic software) -> (output) .c , .h
How to use?
Import -> Browse (get a file) -> ECU(CORETEXM, S32K146) -> add - module configuration(DIO, PORT).
Extra
PortPin direction - choice input, output Port-level value - original value set.
Property->auto - choose pins automatically. Resource - select what machine we use.

## Slide 6: Tresos
Import

## Slide 7: Tresos
Import
Copy basictemplete

## Slide 8: Tresos
Check ECU

## Slide 9: Tresos
Change the resource
S32K146_lqfp 144

## Slide 10: Tresos
Properties
Check the Automatically add

## Slide 11: Tresos
Scratch

## Slide 12: Tresos
ECU name
Check the Automatically add

## Slide 13: Tresos
Module Configuration
Add Port, Dio

## Slide 14: Tresos
Change the resource
S32K146_lqfp 144